## Slide 1: htmaa
sdajani@mit.edu
week 2
group assignment

## Slide 2: embedded programming language workflow
programming efficiency
technical robustness
C
Python
Rust

## Slide 3: embedded development workflow
program complexity
realtime performance
arduino
python

## Slide 4: embedded electronics fabrication workflow
electronic complexity
mechanical reliability
XIAO RP 2040
D21

## Slide 5
Architecture | Example Boards | Toolchain / Workflow | Strengths | Limitations
AVR (8-bit) | ATtiny44, ATmega328 (Arduino Uno) | avr-gcc, avrdude; Arduino IDE for simplified workflow | Mature ecosystem, simple to program, widely taught | Limited memory & speed, not ideal for complex tasks
ARM Cortex-M | SAMD21, STM32, Teensy | arm-none-eabi-gcc, OpenOCD, PlatformIO; Arduino or CircuitPython support | High performance, industry standard, strong debugging tools | Toolchain setup can be complex
RP2040 | Raspberry Pi Pico, XIAO RP2040 | Pico SDK (C/C++), MicroPython, Arduino IDE; custom PIO assembly for peripherals | Flexible, inexpensive, unique PIO hardware for custom protocols | Requires learning PIO for advanced features
ESP8266 / ESP32 | NodeMCU, Sparkfun/Adafruit ESP boards | Espressif SDK/IDF, Arduino IDE, MicroPython | Built-in Wi-Fi/Bluetooth, large community support, IoT-ready | Higher power usage, less deterministic timing
RISC-V | HiFive boards, experimental dev kits | riscv-gnu-toolchain, GDB, newer SDKs | Open-source ISA, growing ecosystem, academic/educational interest | Toolchain less mature, fewer libraries & examples

## Slide 6: workflow examples
SAMD21 (ARM Cortex-M) | RP2040 (Raspberry Pi Pico)
- write code in C/C++ (arduino ide or platformio). - compile with arm-none-eabi-gcc. - upload using openocd via usb or swd debugger. - debug with gdb or serial monitor. | - write code in C/C++ (pico sdk) or micropython. - compile with cmake + gcc toolchain. - drag-and-drop .uf2 file to pico’s usb mass storage device. - (optional) use custom pio assembly for hardware interfaces.
-> ARM workflows emphasize professional-grade debugging, while RP2040 workflows emphasize accessibility and flexibility (drag-and-drop + PIO).

## Slide 7: references
lecture notes
office hours insights
week 2 course website: https://academy.cba.mit.edu/classes/embedded_programming/index.html
ai summarization: https://chatgpt.com/share/68d29349-d7ec-8008-91c5-9abf5e087f6f